## Slide 1: Mobility Tracking
Qiyin Fang, Adam Yu, Michael Zon

## Slide 2: Targeted parameters
Location (GPS)
  Time-stamped GPS coordinates
  What time?

## Slide 3: Sensing requirements
Track mobility
  1000-2000 patients
  Partitioned into cohorts
    1 week out of 3 months continuously tracked
Next step
  Ideally no configuration
  Ideally no charging

## Slide 4: Sensor types
Sensors
  Data is stored locally
    Retrieved after week
  Timestamp, continuous
    Sampling frequency tbd
  Type 1: Bracelet sensor
  Type 2: GPS
Device validation
  Validate accuracy

## Slide 5: Type 1: GPS
Less than $100-150
Travel path
Speed
Distance
Battery life
•Accelerometer activated/deactivated
https://yepzon.com/product/yepzon/

## Slide 6: Type 2: wrist watch
$50-100
Data retrieval
Step count
Distance
Stairs (direction)
Heart rate
Sleep: start, stop
Blood pressure (optional)
Oxygenation (relatively easy)
Accelerator
Gyroscope
Every 3s

## Slide 7: Fitbit Ionic Constraints
Battery life with custom software running for 8 days
Sensor sampling frequency >1/3 Hz
Sensors
  Accelerometer
  Global Positioning System (GPS)
Data Privacy
  Ability to turn off communication capability of device
  Data stored on device
    5 MB storage
      Enough for 7 days of continuous logging at 1/3 Hz
  Direct retrieval of GPA and other identifying data
    No first-party (by company of device) logging of data
Reproducibility of data
  Ability to turn off screen and all user interfacing

## Slide 8: Fitbit Ionic Objectives (in addition to Constraints)
Production at scale
  Potential for automated data retrieval process
  Potential for automated deployment of custom software to all devices
Sensor sampling frequency of 1 Hz
15 MB per sensor
  Enough for 7 days of continuous logging at 1 Hz
Sensors
  Hear rate (beats per minute)
  Body presence (worn or not)
  Barometer
  Gyroscope
  Orientation (quaternion)
  Oxygenation

## Slide 9: Fitbit Ionic Test Components
System with empty program
Barometer
Gyroscope
Accelerometer
Heart Rate
Orientation
Body Presence
Global Positioning System (GPS)
Writing to device

## Slide 10: Fitbit Ionic Battery Test
Each component is individually tested
Each time point records elapsed charge from initially full charge
Sampling Times
  3 hours
  6 hours
  12 hours

## Slide 11: Huawei Watch GT
https://consumer.huawei.com/us/wearables/watch-gt/